## Slide 1: Optical Instruments for Solar Eclipse Measurements Advisor: Dr. Joe Shaw
LOGAN
cARPENTER

## Slide 2: Project Assignments
Spectropolarimeter
  Jon and Logan
Aurora Detector
  Kendra and Logan
Solar radiometer
  All individually

## Slide 3: My mid-term report focus
Measuring the atmospheric optical depth with a Solar Radiometer

## Slide 4: Why would we want to make a Solar Radiometer?
Become familiar with taking data from an instrument. *
Experience calibrating instruments.
Further understanding of atmospheric optics.
Practice for the solar eclipse in 2017
* Photo by Joe Shaw
Notes: -Experience.
-Getting our feet wet in the atmospheric optics world.

## Slide 5: How the solar radiometers work
*
* Number taken from http://www.britannica.com/topic/solar-constant
Earth
Notes: -Light waves propogate
-Solar irradiance at earth

## Slide 6: How the solar radiometers work
Atmospheric extinction.
Greater optical depth means greater extinction.
Notes: -Extinction = absorption + scattering
-Ex of scattering is Rayleigh scattering (blue sky)
-ex of absorption is water vapor (most effective green house gas)
-Higher latitudes means more extinction because of greater optical depth.

## Slide 7: Understanding optical depth
Optical depth =
σ = absorption, scattering, or extinction cross section
gas molecule or particle density
distance along the optical path
Notes: -sigma describes the property of a gas or aerosol to cause extinction.
-N = density
-path
-unit less number that describes the extinction of the light along that particular path
-in order to know the optical depth we need to know the air mass.

## Slide 8: Understanding Air Mass
Air Mass
  Air mass at zenith is 1
  Air mass at the horizon is
Calibration is taking several measurements in varying air masses.
*
* Gratitude to Joe Shaw for the above figure
Notes: -Path with witch light has to pass to reach the observer.
-Angle relative to the zenith

## Slide 9: Using optical depth to find spectral irradiance
Notes: -Irradiance at the point of the observer corresponds to the irradiance outside the atmospheric in a decaying exponential equation.
-do example with E=700 and E_o = 1366

## Slide 10: Calibrating the radiometer by plotting voltages
The solar irradiance correlates to the detector’s voltage
*
* Gracias to Joe Shaw for the figure
Notes: -it is a linear equation of a line
-the y intercept is the exo-atmospheric irradiance
-the slope is the optical depth.

## Slide 11: Radiometer circuit set up
Circuit diagram created by Forrest M. Mims III http://haze.concord.org/spworks.html

## Slide 12: Building and testing the circuit
Difficulty level: 3
Difficulty for Logan: 5.4
(difficulty scale is logarithmic)
The trouble turned out not to be a wire connection, as I thought, but this little guy here.

## Slide 13: Making the casing to hold the radiometer
Battery and circuit board holder
Control switch
Final product

## Slide 14: Next Steps
Calibrate the radiometer by taking measurements from 6am-3pm-ish
Calculate Optical Depth
Check calibration by measuring the optical depth on another day and compare results.

## Slide 15: Acknowledgements
Thanks to Joe Shaw for teaching us about atmospheric optics and helping through the whole process.
Thanks is also due to Joe’s grad students, Dave and Paul, who helped us on a day to day basis.

## Slide 16: Questions? 質問? Preguntas? 问题? Perguntas? الأسئلة?

## Slide 17: Goodbye