## Slide 1: MSU Solar Physics NSF REU Final Presentation
Student: Chace Carlson, Aerospace Engineering Senior at ERAU
Mentor: Dr. Dave Klumpar, Research Professor of Physics and Director, SSEL
Department: Space Science and Engineering Laboratory (SSEL)

## Slide 2: Specialty: Guidance, Navigation, and Control (GNC)
Attitude Determination and Control Systems (ADACS)
Trajectory Planning and Propagation Calculations

## Slide 3: Last Time:
IT-SPINS
  Test Board & ADACS Board
  Ground Station & Dynamic Simulator
  ADACS Telemetry Programming
  MLTAN to RAAN
  Sun Vector Calculations
  Sun Angle Calculations
Mission Concept 1
  Orbital Analysis
Mission Concept 2
  Orbital Analysis

## Slide 4: 1U vs 3U vs 6U

## Slide 5: Mission: IT-SPINS
Ionospheric-Thermospheric Scanning Photometer for Ion-Neutral Studies
  Size: 3U CubeSat
  Launch: October 2017, NASA Educational Launch of Nanosatellites (ELaNA)
  Payload: Stanford Research Institute International Cubesat Tiny Ionospheric Photometer (CTIP)
  Mission: To provide the first 2D tomographic imaging from a 3U research CubeSat. Also, it is MSU’s first CubeSat with an active ADACS system.
  Orbit: Circular, 450 km altitude, 92° Inclination
  Attitude: Spinning @ 2 rpm (about antenna axis)
  Phase: Hardware Development
    Delivery date: May 15, 2017

## Slide 6: IT-SPINS: MAI-400
Maryland Aerospace Inc.
  CubeSat ADACS Systems
Custom MAI-400
  Size: ½ U
  3 reaction wheels
  3 axis magnetometer
  2 IR EHS
  3 electromagnets
  ADACS Computer
  Custom ACS Mode
Photos courtesy of Maryland Aerospace Inc.

## Slide 7: MAI-400: ADACS Telemetry Programming
Work w/software engineers
Integrate with SFC
Problem solving! (Weird integers)
90 EB 11 B6 25 36 42 00 03 00 00 00 00 00 5C 01 00 00 F0 00 10 00 00 00 00 00 00 F0 0F 00 7C F8 80 00 ....
Example ADACS Telemetry:

## Slide 8: MAI-400: Visualization
Dynamic Sim > MATLAB > STK
STK = Systems Tool Kit

## Slide 9: Proposal 1
Size: 6U CubeSat
Launch: Unknown, Early 2018
Mission: Optical signatures of atmospheric gravity waves, traveling atmospheric disturbances, and traveling ionospheric disturbances against the limb far ultraviolet background
Orbit: rp= 400-600 km, ra = 500-600 km, i > 65°
Attitude: 2 modes: spinning @ 2 rpm or nadir pointing
Phase: Proposal Sent to NASA in July

## Slide 10: Mission Concept 1: Power Budget
Calculated average power generated every month, over the course of 1 day
6 Scenarios:
  Worst Orbit Spinning @ 2 rpm
  Average Orbit Spinning @ 2 rpm
  Best Orbit Spinning @ 2 rpm
  Worst Orbit Nadir Pointing
  Average Orbit Nadir Pointing
  Best Orbit Nadir Pointing

## Slide 11: Proposal 2
Size: 6U CubeSat
Launch: Unknown, Summer 2019
Mission: In-situ measurements of the O+ and H+ Temperatures and the electron temperature in the same volume
Orbit: rp= 400-500 km, ra > 800 km, i > 50°
Attitude: 2U facing Nadir, 3U facing Nadir
Phase: Proposal Sent to NASA in July

## Slide 12: Mission Concept 2: Power Budget
Calculated average power generated every month, over the course of 1 day
6 Scenarios:
  Worst Orbit 2U Nadir Facing
  Average Orbit 2U Nadir Facing
  Best Orbit 2U Nadir Facing
  Worst Orbit 3U Nadir Facing
  Average Orbit 3U Nadir Facing
  Best Orbit 3U Nadir Facing

## Slide 13: Solar Power Budget Tutorial
In STK:
Input orbit (worst orbit if mission concept)
Input attitude
Propagate over 1 year, starting on launch date
Generate X,Y, and Z Body Axes Sun Vectors, 1 day per month
  Interval list written via MATLAB
Output vectors as .csv file

## Slide 14: Solar Power Budget Tutorial (cont’d)
In MATLAB:
Run Sun_Vector_Call_Script.m
  Runs Sun_Vector_Funtion.m
  Outputs 12 Excel files, calculating power generated by +X, +Y, +Z, -X, -Y, -Z
Run Summary_Call_Script.m
  Runs Summary_Script.m
  Summarizes all Excel files into 1 compact Excel worksheet

## Slide 15: Solar Power Budget Tutorial (cont’d)
Excel Output for Worst Case Nadir Pointing:
Rinse and Repeat for each scenario (for mission concepts)

## Slide 16: Astrodynamics Lectures

## Slide 17: Conclusion
IT-SPINS
  MAI-400
  Ground Station & Dynamic Simulator
  ADACS Telemetry Programming
Mission Concept 1
  Power Budget
Mission Concept 2
  Power Budget
Solar Power Budget Tutorial
Astrodynamics Lectures

## Slide 18: Questions? https://www.youtube.com/watch?v=lQXHaXujkUY