## Slide 1: Multi-Wavelength Aurora Detector

## Slide 2: Aurora Detector
Aurora images captured at midnight on April 10, 2015, in Delta Junction, Alaska
Notes: Charged particles collide with particles in the upper atmosphere, give off energy in the form of light.

## Slide 3: Aurora Detector
Old Aurora Detector
One detector
Subject to background light
New Aurora Detector
Three detectors
Can isolate aurora from background light
Pure red aurora
Notes: Moonlight. Street lights off of clouds. Don’t beat it up!

## Slide 4: Aurora Detector
Notes: 557.7 and 630

## Slide 5: Aurora Detector
3 Filters, 2 online 1 offline
Notes: Call electronics, not hardware

## Slide 6: Characterizing Optical Filters
Measuring the transmission spectrum
Laser to test angle
Used white light source and VNIR spectrometer
Tilted filter, 0º-8º

## Slide 7: Plotted Wavelength vs. Transmittance
Green Offline
Wavelength (nm)
Transmittance (%)

## Slide 8: Plotted Wavelength vs. Transmittance
Wavelength (nm)
Transmittance (%)

## Slide 9: Average Transmittance

## Slide 10: Setting Up Tube
Front of Tube
Light Filter
Lens
Adjustable
PMT
Notes: Photo Multiplier Tube

## Slide 11: Setting Up Tube
Light Filter
Lens
Adjustable
PMT
Front of Tube

## Slide 12: Finding Focal Point
White light passes through collimating lens
Passes through tube without PMT
Watch dot on sheet of paper
Notes: Collimating

## Slide 13: Field of View
Dark room
Light Source swung around
1º increments, 30 seconds each
Light
Source
Aurora Detector

## Slide 14: Field of View

## Slide 15: After That…
Finish assembly
Heading to Alaska for testing
Preparation for solar eclipse
Notes: Alaska isn’t permanent

## Slide 16
Purple and green aurora. Digital image. NASA Images. NASA, 10 Apr. 2015. Web. <http://www.nasa.gov/sites/default/files/thumbnails/image/20150409-10-sebastiansaarloos.jpg>.
"Glowing Gases - Aurorae." Glowing Gases - Aurorae. N.p., n.d. Web. 10 July 2015. <http://www.atoptics.co.uk/highsky/auror3.htm>.
"Alaska - Google Search." Alaska - Google Search. N.p., n.d. Web. 10 July 2015. <https://www.google.com/search?q=alaska&biw=1301&bih=592&source=lnms&tbm=isch&sa=X&ei=gbyeVcb_EMfKogT30IGQBg&ved=0CAcQ_AUoAg#imgrc=EfbkVkzDpgYeZM%3A>.