## Slide 1: Optical Instruments for Solar Eclipse Measurements Advisor: Dr. Joe Shaw
LOGAN
cARPENTER

## Slide 2: Project Assignments
Spectropolarimeter
  Jon and Logan
Aurora Detector
  Kendra and Logan
Solar radiometer
  Everyone and Logan

## Slide 3: My mid-term report focus
Measuring the atmospheric optical depth with a Solar Radiometer

## Slide 4: Why would we want to make a Solar Radiometer?
Become familiar with taking data from the instrument. *
Experience calibrating instruments.
Further understanding of atmospheric optics.
Practice for the solar eclipse in 2017mEASURING POLARIZATION OF SKYLIGHT. Interpreting the polarization requires knowing the aerosol optical depth. Before and after eclipse.
* Photo by Joe Shaw
Notes: -Experience.
-Getting our feet wet in the atmospheric optics world.

## Slide 5: How the solar radiometers work
*
* Number taken from http://www.britannica.com/topic/solar-constant
Earth
Notes: -Light waves propagate
-Solar irradiance at earth

## Slide 6: How the solar radiometers work
Atmospheric extinction.
Greater optical depth means greater extinction.
Notes: -Extinction = absorption + scattering
-Ex of scattering is Rayleigh scattering (blue sky)
-ex of absorption is water vapor (most effective green house gas)
-Higher latitudes means more extinction because of greater optical depth.

## Slide 7: Understanding optical depth
Optical depth =
σ = absorption, scattering, or extinction cross section
gas molecule or particle density
distance along the optical path
Notes: -sigma describes the property of a gas or aerosol to cause extinction.
-N = density
-path
-unit less number that describes the extinction of the light along that particular path
-in order to know the optical depth we need to know the air mass.

## Slide 8: Understanding Air Mass
Air Mass
  Air mass at zenith is 1
  Air mass at the horizon is
Calibration is taking several measurements in varying air masses.
*
* Gratitude to Joe Shaw for the above figure
Notes: -Path with witch light has to pass to reach the observer.
-Angle relative to the zenith

## Slide 9: Using optical depth to find spectral irradiance
Notes: -Irradiance at the point of the observer corresponds to the irradiance outside the atmospheric in a decaying exponential equation.
-do example with E=700 and E_o = 1366

## Slide 10: Calibrating the radiometer by plotting voltages
The solar irradiance correlates to the detector’s voltage
*
* Gracias to Joe Shaw for the figure
Notes: -it is a linear equation of a line
-the y intercept is the exo-atmospheric irradiance
-the slope is the optical depth.

## Slide 11: Brief Explanation of LEDs
P-type
N-type
Conduction Band
Valence Band
Notes: -Semiconductor (Gallium Nitride)
-Electroluminescence
-Band Gap determines color

## Slide 12: How LSDs work
Light. Sucking. Diode.
Notes: -Electron excited into Conduction zone
-Of no Effect unless charge is running through
-The injection current doesn’t reach the threshold to emit light

## Slide 13: Solar Radiometer in a nutshell
Reading from voltmeter
Reading from voltmeter
Notes: We hook up a source and are then able to measure the output.

## Slide 14: Radiometer circuit set up
Circuit diagram created by Forrest M. Mims III http://haze.concord.org/spworks.html

## Slide 15: Building and testing the circuit
Difficulty level: 3
Difficulty for Logan: 5.4
(difficulty scale is logarithmic)
The trouble turned out not to be a wire connection, as I thought, but this little guy here.

## Slide 16: Making the casing to hold the radiometer
Battery and circuit board holder
Control switch
Final product

## Slide 17: Taking Readings
Pic of Voltage vs Time

## Slide 18: Calibration
Picture of log(voltage) vs air mass

## Slide 19: Calculating the Optical Depth
= optical depth
exo-atmospheric reading

## Slide 20: Future Work
Calculate the spectral irradiance for the wavelengths of the LED.
Calculate different optical depths.

## Slide 21: Acknowledgements
Thanks to Joe Shaw for teaching us about atmospheric optics and helping through the whole process.
Thanks is also due to Joe’s grad students, Dave and Paul, who helped us on a day to day basis.

## Slide 22: Questions? 質問? Preguntas? 问题? Perguntas? الأسئلة?