## Slide 1: Space Weather and Radiation Multi-point Magnetometry (SWaRMM): Cube Satellite Mission Design Study
Tyler Croteau
MSU Solar Physics REU: SSEL
Mentor: Dr. Klumpar

## Slide 2: Outline
Introduction to CubeSats
Mission Focus
  Mission Science
Mission Concept Characterization
  Orbit analysis
  Structure
  Budget Estimates
  Command and Data Handling
  Attitude Determination and Control
Outcomes

## Slide 3: CubeSat Introduction
Class of Nanosatellite
  1U: (10x10x10 cm)
  2U: (20x10x10 cm)
  3U: (30x10x10 cm)
Deploy from P-POD
  Low Earth Orbit (LEO)
  Science and space
  weather applications
MSU’s FIREBIRD 3 and 4
P-POD Mounted to Minotaur Launch Vehicle

## Slide 4: SWaRMM Mission
Primary Objective: Conduct space weather science that requires multipoint measurements
  Electromagnetic Ion Cyclotron (EMIC) waves at high latitude
  Boom deployed mini fluxgate magnetometer
Secondary Objective: Demonstrate the capabilities of a swarm of 0.5U CubeSats
  Uncommon
  Low Cost
  Low Power

## Slide 5: EMIC Waves
Magnetosphere
  Plasma instabilities
  Energy from anisotropic protons (0.1-5 Hz)
    transferred from particles to waves when gyrofrequency matches Doppler shifted wave frequency
  Amplification based on time of propagation through finite growth region
    Multipoint measurements
    Reduction in density of magnetic field in propagation region
    Off-equator local minimum magnetic field regions not yet been extensively studied

## Slide 7: Fluxgate Magnetometer
2 half cores of ring with 2 coil windings
  Current flows through windings
No External field
  Cores saturate at same
  time
External Field
  Core fields do not cancel
  and induce voltage
Notes:   1 half core generates field in same direction as the external field while the other generates in the opposite

## Slide 8: Structure
0.5U Size (5x10x10 cm)
650 grams per CubeSat
  6 units in one PPOD
Utilize MSU Flight Heritage
  FIREBIRD 3 and 4
  ICE
(1x1 cm) Solar Cells
0.5U SolidWorks Rendering

## Slide 9: Swarm Design and Orbit Analysis
String Of Pearls
  Slow Separation
  Linear Orbit dynamics
  allows passively
  stable formation flying
Constraints
  6-12 0.5U CubeSats
  400-600 km circular LEO
  High latitude
  inclination 60-80 deg
STK 12 Sat Deployment
Orbit Inclination

## Slide 10: Mass Budget
Must be < 650g/CubeSat
Scaled from FIREBIRD flight heritage
5.14g reserve with worst case uncertainties

## Slide 11: Electrical Power System (EPS)
Primary: Space rated Photovoltaics
Secondary: Lithium Ion
  3.3V regulated power
  Direct energy transfer from solar cells
94.6 min Orbital Period
  Assume 0.65 sunlit orbit fraction = 61.5 min sunlight/orbit

## Slide 12: EPS Sizing
Need 1.04W average solar array power

## Slide 13: Command and Data Handleing (C&DH)
5Hz EMIC waves
  10Hz sample rate
  3 axis magnetometer:
  16 bits per axis
Given 4GB of NAND-Flash
  740 days without overwriting
  data
Link Design
  Feasibility of a radio link:
    FIREBIRD flight heritage

## Slide 14: Downlink
Collect around 2%
total data per day
per CubeSat
  Consider two ground
  stations
Campaign Mode
  Down-link Low-res data for event spikes before High-res

## Slide 15: Attitude Determination and Control (ADCS)
Investigate gravity gradient
  Tip mass on deployed boom
  Nadir pointing aligned
    with max moment of inertia
Hysteresis rods
  Dampen gyration

## Slide 16: Conclusions
6 CubeSat 0.5U Constellation: Feasible
Investigate Further
  EPS and solar panel alternatives
  ADCS gravity gradient options

## Slide 17: Acknowledgments
Dave Klumpar - Advisor
Keith Mashburn – SSEL Systems Engineer
Kevin Zack – SSEL Grad Student
Matthew Handley – SSEL Grad Student
All of the SSEL team
References
[1]Maria de Soria-Santacruz, Electromagnetic Ion Cyclotron (EMIC) Waves for Radiation Belt Remediation Applications, Space Propulsion Laboratory, MIT, 2015.
[2] Wiley, Observing the Birkeland currents, ScienceDaily. ScienceDaily, 6 October 2014.
[3] Wertz, J.R., and Larson, W.J., Space Mission Anaylsis and Design, 3rd ed., Microcosm, El Segundo, CA, 1999, pp. 353-518.
[4] Electdom Matandirotya, and Robert R. Van Zyl, Evaluation of a Commercial-Off-the- Shelf Fluxgate Magnetometer for CubeSat Space Magnetometry, JoSS, Vol.2, No.1, pp. 133-146.
[5]Erich Bender, An Analysis of Stabilizing 3U CubeSats Using Gravity Gradient Techniques, California Polytechnic State University, San Luis Obispo, 2011, pp. 1-24.
[6] David T. Gerhardt, Passive Magnetic Attitude Control for CubeSat Spacecraft, University of Colorado, Boulder, CO, 24th Annual AIAA/USU SSC10.

## Slide 18: Questions