## Slide 1: Space Engineering Mission Design: CubeSat Swarm
Tyler Croteau
MSU Solar Physics REU: SSEL
Mentor: Dr. Klumpar

## Slide 2: Outline
Introduction to CubeSats
Mission Focus
Introduction to Mission and Design Process
Mission Concept Characterization
  Orbit analysis
  Budget Estimates
  Link design
  Communication Architecture
Timeline

## Slide 3: CubeSat Introduction
Class of Nanosatellite
  1U: (10x10x10 cm)
  2U: (20x10x10 cm)
  3U: (30x10x10 cm)
Deploy from P-POD
  Low Earth Orbit (LEO)
  Science and space
  weather applications
MSU’s FIREBIRD 3 and 4
P-POD Mounted to Minotaur Launch Vehicle

## Slide 4: The Mission: CubeSat Swarm
Primary Objective: Conduct space weather science that requires multipoint measurements
  Electromagnetic Ion Cyclotron (EMIC) waves at high latitude
  Boom deployed magnetometer
Secondary Objective: Demonstrate the capabilities of a swarm of 0.5U CubeSats
  Uncommon
  Low Cost
  Low Power
0.5U SolidWorks Rendering

## Slide 5: Introduction to Mission Design
Define Objectives
Preliminary Estimates
  Functional: Orbit, Power
  Operational: Data, Link, Communication architecture
  Constraints: Costs
Characterization and Alternatives
  Trade Studies
  Produce Budgets
Select Design for Proposal

## Slide 6: Swarm Design and Orbit Analysis
String Of Pearls
  Slow Separation
  Linear Orbit dynamics
  allows passively
  stable formation flying
Constraints
  6-12 0.5U CubeSats
  400-600 km circular LEO
  High latitude
  inclination 60-80 deg
STK 12 Sat Deployment
Orbit Inclination

## Slide 8: Preliminary Budgets
Assumptions
  0.5W payload
    Fluxgate Magnetometer
  10 Hz sample rate
    Range of EMIC events
  12 bit measurements
  Want 30 measurements/sec
  =360 bits/sec

## Slide 9: Power Budget
Orbit Average Power (OAP) – Average Power Used
In general OAP = 60% *(Power from one panel)
  1x1cm cells at 37% efficiency
  1361W/m^2*(0.37)*(0.0044m^2) = 2.2W
  1361W/m^2*(0.37)*(0.0017m^2) = 0.85W
CTJ Photovoltaic Cell Characteristics
SolAero CTJ Cell
STK Solar Panel Tool Model

## Slide 10
Comparison to STK:
%60 of 2.2W – 0.7 W = 600 mW
%60 of 0.85W – 0.4W = 100 mW
Estimated Budget:
2.5W – 0.5W = +2W

## Slide 11: Link Design
Determine feasibility of a radio link
  Relationship between data rate, antennae size, propagation path length, transmitter power
  Defined by Link Budget:

## Slide 12: Communications Architecture
Individual ground station relays Vs. Crosslink communications
  Trade Studies:
    Link distance
    Vs. Link bandwidth
    Frequency
    Vs. Number of contacts
    Short range wireless
    Vs. Long range crosslinks
Prefer individual autonomous satellites

## Slide 13: Timeline
Mission Focus
Orbit Analysis
Budget Characterization
  Power
  Link
  Data
  Telemetry
  Mass
  Trade Studies
Proposal
Complete
In Progress
Not Started

## Slide 14: Acknowledgments
Dave Klumpar - Advisor
Keith Mashburn – SSEL Systems Engineer
Kevin Zack – SSEL Grad Student
Matthew Handley – SSEL Grad Student

## Slide 15: Questions

## Slide 16: Bonus Slides

## Slide 17: EMIC Waves
Magnetosphere
  Plasma instabilities
  Energy from anisotropic protons (0.1-5 Hz)
    transferred from particles to waves when gyrofrequency matches Doppler shifted wave frequency
  Amplification based on time of propagation through finite growth region
    Multipoint measurements
    Reduction in density of magnetic field in propagation region
    Off-equator local minimum magnetic field regions not yet been extensively studied

## Slide 19: Fluxgate Magnetometer
2 half cores of ring with 2 coil windings
  Current flows through windings
  1 half core generates field in same direction as the external field while the other generates in the opposite
No External field
  Cores saturate at same
  time
External Field
  Core fields do not cancel
  and induce voltage