## Slide 1
Explosive Events in the Quiet Sun
Extreme Ultraviolet Imaging Spectroscopy
Instrumentation and Observations

## Slide 2: Abstract
Transition Region Explosive Event (EE) is the name for large spectroscopic velocities observed in extreme ultraviolet emission lines formed between 50,000K and 500,000K in the solar atmosphere. Thought to be powered by magnetic reconnection, they may contribute to the mass and energy balance of the hot solar corona. Understanding of these transient events is hampered by lack of rapid, high resolution combined spatial and spectral measurements. We present EE observations and analysis from the Multi-Order Solar EUV Spectrograph (MOSES) that open the door for true high speed imaging spectroscopy in the solar transition region.

## Slide 3: The coronal heating problem
Dissipation of magnetic energy
Active Sun
  Active Regions
Quiet Sun
  ??
Notes: X-ray (HOT!) emission
Solar Cycle 11 year peak to peak

## Slide 4: High Resolution Telescope and Spectrograph Observations
Small explosions at the base of the corona
Supersonic spectroscopic velocities
Average Properties:
  100 km/s
  2” (1500 km)
  60 s lifetimes
  600 s-1 birthrate
Dere 1989
CIV λ1550
logT = 105
Notes: At log T = 10^5,

## Slide 5: HRTS Observations
Associated with changes in photospheric magnetic flux
Likely powered by magnetic reconnection
HRTS EEs lie on the boundary of the quiet
sun magnetic network
Dere 1991
Notes: The picture here is

## Slide 6: Magnetic Reconnection
Converts magnetic energy to plasma mechanical energy
A little hard to see in
the corona…
NASA/Goddard Space Flight Center
Scientific Visualization Studio - TRACE
Tom Bridgman
Notes: Reconnection often associated with flares in active regions…
Terrible line of sight problems looking at dark things in a bright oprically thin medium…

## Slide 7: EE’s and reconnection
If EE’s are observational signatures of reconnection they have tremendous diagnostic value:
Density 10x greater in
TR, EM 100x greater.
EE’s extremely common
Parker 1957
Petschek 1964
Notes: Rudolf A. Treumann1,2* and Wolfgang Baumjohann3
Front. Phys., 31 December 2013
https://doi.org/10.3389/fphy.2013.00031

## Slide 8: EE emission traces reconnecting field
Innes et. al. 1997
Notes: The significance here is that authors assert that the plasma shows the field lines. Thus ee’s are direct observations of reconnecting field.
>Innes 1997 – Yes! Sort of…
>Slightly different than flares and BP’s – weak mixed polarity fields rather than bipolar fields.

## Slide 9: EE Reconnection - Petschek
Innes and Toth 1999
  Petschek
  Bi Directional Jets,
  no core
Dere 1989

## Slide 10: EE Reconnection - Plasmoid
Innes et al 2015
  Plasmoid instability
  Core dominates after initial period of bi directional jets
Notes: Add points, or add another slide, regarding the fact that some line profiles show core brightening, and some do not.

## Slide 11: Observational Hurdles
Winebarger et. al. 2002
Notes: FIX THIS SLIDE UP!!

## Slide 12: Multi-Order Solar EUV Spectrograph (MOSES)
Imaging spectrograph designed to measure spectra in a single snapshot over a wide FOV
Notes: 1.) Sounding Rocket Mission
2.) m=0 is total intensity at all wavelengths, gives spatial location of emission.
3.) dispersed images show counts at location which depends on WHERE the emission came from, and the WAVELENGTH of the emission.
4.) Objects appearing at a different location in the dispersed orders relative to zero indicates off line center emission.
5.) Multilayer ideally restricts the passband to a single spectral line  emission observed off line center is due to doppler shifts.

## Slide 13
MOSES-I
February 8 2006
10’ x 20’
0.59” pixels
30 km/s/pix
Dispersion along x
30.4 nm

## Slide 14
27 Exposures from 0.25-24 s
  Avg. cadence is
  ~ 10 s
Dark Subtraction
Flatfield
Coregistration
Data Reduction
m = +1
m = 0
m = -1
Notes: 0.)Change this movie: color scheme? Apple Universal?
0’.)These imges are log scaled. Black regions are missing data.
1.) Coregistration of the dispersed images to the m=0 image ensures that line center emission appears in the same pixel in each image.
2.) Now we go looking for compact sources with disparity between dispersed and non dispersed intensities.

## Slide 15: He II λ304 Spectral Line
Andretta et. al.
2000
log T = 4.9
vT = 13 km/s
(1 sigma)
Notes: He II anomalous intensity

## Slide 16: Difference Images

## Slide 17: Wavelet Transform
Coarse Scales
Fine scales
Medium scales

## Slide 18: Small Scale Difference Images

## Slide 23
Raw Data

## Slide 24
Wavelet Transform
Small Scales

## Slide 25
No Doppler Shift
Red Shift Only
Blue Shift Only?
Bi Directional Shifts
Shifts 3-4 pixels
≈ 100 km/s
No Line Core

## Slide 26: Point Spread Functions
Notes: Wavelet Transform
Show PSFS, brief method of reconstruction:
  reconstructs psfs, respects the noise

## Slide 27: PSF Partial Reconstruction
Notes: The key here is that only a small subset of wavelet coefficients is sufficient to explain the intensity distribution corresponding to the EE. In the inversions then only these coefficients should contribute.
Make this a movie, instead?
Show all psfs?
Show psf profiles, angular/spectral resolution? – YES!

## Slide 28: PSF Estimates

## Slide 29
Notes: Forward model is fairly convincing.
How about the inverse problem?

## Slide 30: Inversions
MOSES imaging equation:
MOSES images are projections of the
solar spectral radiance ν(x,y,λ)
The inverse problem of
reconstruction from projection
data is called tomography
MOSES is a three projection
tomographic imager
Fox et al 2010
Notes: ν(x,y,λ) is the solar spectral radiance
Tomography – same as cat scan

## Slide 31: Inversion method: (S)MART
Guess
Project through Guess to simulate Data
Divide data by projection
Back project to form Correction
Multiply Guess by Correction1/3
Iterate to convergence
λ
x
Notes: 1.) MOSES is a few projection tomography problem.
2.) Tomographic inversion is automated, treats all objects in the same way, allows estimation of a spectra for each space pixel.
3.) MART is standard reconstruction technique – solution is always positive and missing data is easier to deal with that using, say, fourier backprojection.
4.) Reconstruction artifacts are inevitable. Reconstructing data filtered to contain only the object scales of interest seems to reduce artifacts  inversion applied to high pass filtered data.
5.) PSF deconvolution applied prior to filtering.

## Slide 32: Inversion Results

## Slide 33: Inversion Results

## Slide 34: Inversion Results
Averaged
Line Profile

## Slide 35: Inversion Results
Averaged
Line Profile
Slice through
reconstructed
radiance

## Slide 36: MART + Partial Reconstruction
Only a handful of wavelet coefficients
describe the explosive event
Notes: Also tacked on a deconvolution… another slide for this?

## Slide 37: Partial Reconstruction

## Slide 38: Inversion Results 2
MART + Partial Reconstruction + Deconvolution

## Slide 39: Inversion Results 2

## Slide 40: Inversion Results 2

## Slide 41: Inversion Results 2

## Slide 43: Evolution
No acceleration phase
No sky plane motion
No core brightening

## Slide 44: Spatial Distribution
Notes: Small events
Line wing dominated – Petschek
Need to clean this shit up
Similar morphology. Hmmm….

## Slide 45: Conclusions on EEs
This is the clearest example to my knowledge of an explosive event spectral line profile consistent with Petschek reconnection
EE’s common in He II λ304. Only one prior published report (Fox et. al. 2010)
Explosive events in He II are line wing dominated. This suggests the plasmoid instability is not occurring – why?
All observed EE’s are associated with a brightening
Complicated, rapid sky plane motions are present in some events. It is likely these would prove impossible to investigate using slit spectroscopes.
Motion is not rotational

## Slide 46: Conclusions on MOSES
Excellent tool for explosive event observations, with or without inversions
For the first time we have shown how to obtain accurate EE line profiles through inversion of MOSES data.
I hope this work contributes to our understanding of existing and future MOSES data, as well that of the upcoming ESIS.

## Slide 47: Further Work
Automatic event detection and classification
Energetics – need densities
“At the moment, the debate is still open as to where the primary energy in-put site is and can probably only be resolved by high resolution simultaneous spectroscopic imaging from the chromosphere to the corona”
      Innes and Teriaca 2012